# NEW BETA VERSION SUBMISSION

## PRODUCT   			uZ CGRS

## VERSION #   		uZ_CJ10 (application);  BT_0A16 (boot)

## Submission Date  		10/22/2001

## (From uZ_CJ00 to uZ_CJ10)

###### Change Descriptions

- Resolved possible issue with the output of NMEA, raw data and BINEX data outputs from becoming contaminated.

- Return NAK for imcomplete $PASHS,OUT,x,MET or $PASHS,OUT,x,TLT messages.

- Add the functionality for $PASHS,OUT,c to turn off MET/TLT output where ‘c’ is the port.

- Fixed possible incorrect display response from $PASHQ,PAR command because of extra \0.

- Added command $PASHS,DRI to control only data recording interval for logging in the receiver. Added command $PASHS,DOI to control only serial port output interval for

$PASHS,OUT,c messages

$PASHS,RCI,i where ‘i’ is the interval, will set both data recording interval and serial port output interval as before. All other serial commands or receiver screen inputs will only change the data recording interval.

- Fixed the problem of not saving BINEX settings with the $PASHS,SAV command.  (Note: for uZCGRS hardware, $PASHS,SAV is ALWAYS set to Y or YES).

- Resolved the issue of Z-modem downloading turning off real-time output on any port when activated.  Now Z-modem downloading will only turn off real time output on the port you are downloading from when using the Z-modem protocol.

###### Known Issues:

- The commands

$PASHS,BNX,ON and $PASHS,BNX,OFF

Will return an ACK but will not perform any function.  To activate or deactivate BINEX output, a user must specify the port as well.  For example:

$PASHS,BNX,ON,A

$PASHS,BNX,OFF,A