# R7/5700 GPS Receiver UNAVCO System					            www.unavco.org

Standard system includes:

-R7/5700 receiver *				Rx QC by:			Date:

-Zephyr geodetic antenna *

## -Transport case *

* Identified by system number.

-10m TNC-TNC antenna cable

-Download/power cable

-North-American AC power cord

-AC power supply

-DC power cable – ruggedized, fused, and with ring terminals

-128Mb (or greater) Industrial compact flashcard (in receiver)

-Copy of this list

Optional items in system box, per request only:

-Internal batteries

-18Ah gel cell battery

-Battery charger

-Solar panel

2/28/08

### - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

### Useful Information

LED Indicators:

|  | Logging/memory LED (yellow) | Satellite tracking LED (red) | Power LEDs (green=in use or yellow=standby)* |
| --- | --- | --- | --- |
| On | Data are being logged | Receiver in monitor mode | Healthy |
| 5 sec flash while OFF | Session programmed in receiver | N/A | N/A |
| Slow (1 sec) flash | Enough Fast Static data have been logged (per preset criteria) | Tracking four or more satellites | N/A |
| Fast flash | Warning-low memory | Tracking three or less satellites | Low power |
| Off | Not logging data | Not tracking any satellites | No power source present |

*External batteries override internal batteries.

The 5700 receiver is programmed at UNAVCO for automatic logging of 24 hour UTC files, 15 second sample rate, 5 degree elevation mask. To change the default settings, use the Configuration Toolbox (C-Tools) software available from facility.unavco.org.  Programming the 5700 correctly is critical for collecting the desired data. The process is not trivial, and a well understood sequence must be followed to ensure proper data collection. The recommended sequence is:

 1. Use C-Tools v4.0 or newer to get the power_up configuration file from the receiver. Earlier versions of C-Tools do not support Time Activation, which is necessary to program sessions.

2. Modify the file as desired.

3. Save the file to the computer. 
4. Close (completely exit) C-Tools. 
5. Perform a hard reset of the receiver and format the compact flashcard by holding the receiver power button down for 30 seconds. CAUTION: Any data on the compact flashcard will be erased!
6. Open the saved configuration file in C-Tools. 
7. Transmit the configuration file to the receiver. 
8. Close C-Tools. 
9. Test run the receiver to verify proper operation prior to actual fieldwork.

Current support information, including specific 5700 receiver documentation, is available on the UNAVCO web page: facility.unavco.org                      		Support questions? Email support@unavco.org